## Slide 1: MINI PROJECT
ECU1: Vehicle Status Display and Control Interface

## Slide 2
About project
01
CONTENTS
CONTENTS
Components
02
Software
03
Working
04

## Slide 3
About project
01

## Slide 4
About Project Phases
1
4
2
3
check wheather the vehicle staus is active or not.
Check vehicle state
Design HMI interface to display all associated data.
Design HMI
Read different signals from different sensors.
Read signals
Display all data recived from parts onto the HMI.
Show data on HMI

## Slide 5
COMPONENTS
02

## Slide 6
ESP-32

## Slide 7
Features of esp32
Dual-Core Processor
Wi-Fi and Bluetooth
GPIO Pins
ADC/DAC
High Peripheral Support
Flash Memory(4MB)

## Slide 8
CAN transceiver
Features of CAN
Communication Protocol
ISO Standard(ISO 11898)
Efficient Data Transfer
Error Detection
Data transfer upto 1 Mbit/second

## Slide 9
COMPONENTS
Preentations are communication tools.

## Slide 10
SOFTWARE
AND
LIBRARIES
03

## Slide 11
IDE
Arduino IDE used to program and flash code into the ESP32 board
1.ESP32 board extension
2.CAN controller header(CAN.h)
3.HMI header file
Libraries

## Slide 12
WORKING
04

## Slide 13
WORKING PHASES
Setting up CAN communication between boards.
Setting up CAN
01
02
04
03
Reading and monitoring signals from differnt boards.
Monitoring values
Verify and finalise collected data.
Finalise data
Display vehicle staus and information on HMI.
Display on HMI

## Slide 14
Setting up CAN
Include header
set CAN pins
start CAN communication at 500kbs
sending data through can
Send data over CAN
#include<CAN.h>
CAN.setpins(2,4);
if(!CAN.begin(500000)){
Serial.println("CAN failed");
while(1);
} else {
Serial.println("CAN Started");
}
CAN.beginPacket(0x11);
CAN.write((uint8_t*)&value,sizeof(value));
CAN.endpacket();

## Slide 15
.Receive data over CAN
if(CAN.parsePacket()){
if(CAN.packetId()==0x12){
CAN.read((uint8_t*)&data,sizeof(data));
}
}
Serial.println(data);

## Slide 16
void can_read(){
if(CAN.parsePacket()){
if(CAN.packetId()==0x12){
CAN.read((uint8_t*)&data,sizeof(data));
}
}
Serial.println(data);
}
void can_read(){
CAN.beginPacket(0x11);
CAN.write((uint8_t*)&value,sizeof(value));
CAN.endpacket();
}
#include<CAN.h>
#define SPEED 5000000
int data;
int value = 10;
void setup() {
Serial.begin(9600);
CAN.setpins(2,4);
if(!CAN.begin(SPEED)){
Serial.println("CAN failed");
while(1);
} else {
Serial.println("CAN Started");
}
}
void loop() {
can_read();
can_send();
}
Sample code

## Slide 17
NEXT TASK
Establish CAN communication between different ECU’s
Send vehicle status through CAN
Monitor incoming values using CAN bus interface
Design HMI interface to display each values on appropriate fields

## Slide 18
HMI DESIGN
I am using Nextion intelligent HMI display
TFT Touch Display:
Serial Communication
Reduced Development Time:
Low Power Consumption
Nextion Editor:

## Slide 20
SAMPLE CODE 2 (using multiple core and a byte array)
CAN pin setting and initialization
CAN.setPins(18,19);
Serial.begin(115200);
if(!CAN.begin(500E3)){
Serial.println("can failed");
while(1);
}
Serial.println("CAN SETUP");
Assigning task to each cores of esp32
xTaskCreatePinnedToCore(send, "send msg", 1024, NULL, 1, NULL, 0);
xTaskCreatePinnedToCore(recv, "recive", 1024, NULL, 1, NULL, 1);

## Slide 21
Sending button starus using core 1 of esp
void core_0(void *parameters){
while(1){
unsigned long time= millis();
if(time - current_time >= SEND_TIME){
array[0] = read();
CAN.beginPacket(0x01);
for(i=0;i<8;i++){
CAN.write(array[i]);
}
CAN.endPacket();
Serial.println("message sent");
current_time = time;
}
vTaskDelay(200 / portTICK_PERIOD_MS);
}
}

## Slide 22
Reading incoming messages using CAN on core 2 of esp32
void core_1(void *parameters){
while(1){
Serial.print("core 1\n");
if(CAN.parsePacket()){
if(CAN.packetId()==0x01){
for(i=0;i<8;i++){
array[i] = CAN.read();
}
}
}
Serial.println(array[0]);
Serial.println(array[1]);
Serial.println(array[2]);
vTaskDelay(100 / portTICK_PERIOD_MS);
}
}

## Slide 23
THANKS
Presented by
Adin N S